## Slide 1: Step 1
Setup a TFTP( or FTP or HTTP)
Execute it
Notes: © 2007 Welltech Computer Co., Ltd. All right reserved.

## Slide 2
Step 2
Mac address
Account Number
Password
ATA can register to three different sip server
Ph1realm1 is for the first account
Ph1realm2 is for the second account
Ph1realm3 is for the third account
Ph2 is for the phone2 of 172
Set the Maclist File
Notes: © 2007 Welltech Computer Co., Ltd. All right reserved.

## Slide 3
Step 3
SIP Server IP
All the mutual setting can be set here
You can Set $ for ATA to ingore it
Set the StandwardCFG File
Notes: © 2007 Welltech Computer Co., Ltd. All right reserved.

## Slide 4
Step 4
Select the path of Mac and standard file
And clisk “ Start” to generate the configured file
Set the excryption key as welltech
Generate the configured File
Notes: © 2007 Welltech Computer Co., Ltd. All right reserved.

## Slide 5
Step 5
The configured file is generated here with the
Mac as the file name
Copy it to the folder of TFTP
Notes: © 2007 Welltech Computer Co., Ltd. All right reserved.

## Slide 6
Step 6
Select the type of your server
And set the ip address of it
Notes: © 2007 Welltech Computer Co., Ltd. All right reserved.